Introduction of Equipment

1. Boom "Beach Boom" (Vikoma, U.K.) 【Stored at Tokyo Bay Base (Chiba Prefecture, Japan)】

When afloat, Shoreguardian has excellent wave following characteristics because of its air buoyancy/water ballast tube design. When aground, the vertical perforated inner membrane acts as a tension member and prevents the boom from rolling when grounded. Due to these features, Shoreguardian has excellent stability and sealing characteristics.

2. Oil Skimmer “Tarantula”（Vikoma U.K.）

【Stored at Seto Inland Sea Base (Okayama Prefecture, Japan)】

Tarantula incorporates two Desmi DOP-250 pumps which deliver a maximum capacity of 250 m2/h and can develop discharge pressures up to 10 bar while maintaining nearly maximum flow. It is capable of recovering a wide range of oils even with high viscosities. Net weight is about 5,500 kg.

※Check and adjustment of hydraulic pressure are recommended after transfer, as hydraulic pressure occasionally cannot rise sufficiently due to aged deterioration.

3. Oil Skimmer “Desmi 250” (Desmi Ro-Clean, Denmark)

【Stored at Singapore Base and Abu Dhabi Base】

It has a weir type device with a vertical Archimedes screw head to recover floating oil. It is supported in the water by three floats. Its designed pump capacity is 50 kls per hour. This Desmi 250 skimmer is suitable to recover middle-high viscosity oils.

Container: 2.8mL　×　2.2mW　×　2.3mH,  Weight: 2.8ton

4．Boom "Hi-Sprint 1500" (Vikoma, U.K.) 【Stored at Al-Khafji Base】

Freeboard : 60 cm, Draft : 90 cm, Unicon-joint 250 m/10 f container, 
500 metres can be deployed in less than twenty minutes. This speed is due to the innovative features of single point inflation, a continuous air feeder sleeve, and a one way valve to every 3 m chamber. The boom's continuous cylindrical shape, coupled with low air inflation pressure increases flexibility, and produces a very responsive containment system. The high buoyancy to weight ratio gives good wave following capability.

5. Oil Skimmer “GT 185-6” (Lamor, Finland) 【Stored at Al-Kahfji Base and Malaysia Base】

This skimmer consists of a three floating frame on which mounted a weir pump unit. The pump unit has an upward facing suction inlet fitted with a hopper, which allow users to control the upper edge of the hopper, relative to the oil/water interface.

Container: 3.0mL　×　2.4mW　×　2.6mH,  Weight: 2.8ton

6.　Beach Cleaner “Power Vac” (Vikoma, U.K.)

【Stored at Al-Khafji Base and Abu Dhabi Base】

Powervac is a self contained, simple to use, one man operated oil recovery system and is a trolley mounted unit to recover oil to a standard 45 gallon barrel or optional hopper. It is designed for the removal of oiled sands, muds and debris up to a rate of 30 tonnes per hour. The high-pressure water jet can use salt or freshwater.